Tesla Coil Theory

    Line voltage is stepped up by the high-voltage transformer to a
    magnitude sufficient to charge the capacitor and force the spark gap to
    break down.  This action is repeated at the 60 hertz line frequency.

    Efficient energy transfer is enhanced by choosing a capacitor whose
    impedance is equal to that of the secondary winding.

    Essentially, the capacitor and tesla coil primary form one pair of tank
    circuits: When the spark gap arcs, the momentary short circuit created
    dumps the capacitor's charge into the coil's primary.  The resulting
    L-C circuit rings as the charge oscillates back and forth between the
    capacitor and the coil.  The oscillations decrease in amplitude as the
    charge is dissipated by resistance.  The ringing generates what is
    referred to as a "damped wave".  The next half-cycle of 60-hz recharges
    the capacitor, starting the process anew.  a train of hi-frequency
    waves, spaced at 60-hz intervals, is the product.

    Resonance must be achieved to effect ringing: This demands the
    capacitor and primary have the same reactance: x(L) = x(C) the circuit
    resistance (capacitor, coil and intermediate wiring) limits the overall
    efficiency of the tank circuit.  efficiency is rated in terms of
    "quality factor", represented as 'Q': Q = w(L)/r = x(C)/r

    Increasing resistance reduces Q, thereby reducing efficiency.  The
    effect is minimized by winding the primary with a few turns of heavy
    conductor, well-spaced, over a large radius form - the larger the
    better.  The capacitor size and construction also bear upon Q.  The
    physical size and area should be minimized.  This, however, works
    against large capacitance values and dictates the coil be wound with
    more turns.  The goal, then, is to achieve a workable range of
    component specifications rather than to strive for overly close
    tolerances.  Coils often are wound with tapped primaries to facilitate
    fine tuning.

    The secondary coil is situated both electrically and physically within
    the primary.  The secondary and its discharge electrode, generally a
    sphere or toroid, make up the second tuned circuit.  The winding
    supplies inductance; The capacitor is created by the electrode and the
    (earth) ground-plane.  Air is the dielectric.  Most tesla coils employ
    secondaries of 1/4-wavelength at their operating frequencies.  This
    establishes a configuration with maximum current at zero voltage with
    minimum current at the electrode.  this situation proves to be
    beneficial, in that it enhances coupling with the high current primary,
    avoids arcing between the primary and secondary and generates the
    desired high voltage at the top end.

    The "Bi-polar Tesla Coil is a 1/2-wave variation on the Tesla Coil.  It
    possesses the essential tesla coil operational characteristics, but it
    employs a horizontally placed secondary with discharge electrodes at
    both ends and a primary at the center.  The Bi-polar primary sometimes
    is merely a pair of taps on the secondary (an autotransformer).  The
    1/2- wave arrangement affords a coil with maximum discharge at each end
    and a virtual ground at the midpoint of the winding(s).

    The Oudin coil is similar to the Tesla coil except that the inner most
    turn of the primary and the bottom of the secondary are both connected
    to ground.  Oudin coils usually have a characteristic cone shape with
    the large end sitting on the ground.  This configuration almost
    eliminates the chance of primary to secondary arcing and the loss of
    energy by corona at the top windings of the secondary coil.  However,
    many neon sign transformers simply can not be used in this way, unless
    you use only half the output (ie use only one of the two High-voltage
    outlets) thus reducing spark length considerably.