From rwstephens@ptbo.igs.net Wed Apr 24 19:55:58 1996

ltc01rws.jpg
This is my largest TC to date. This unit stands 9 feet tall to top of 
toroid discharge terminal as shown here. I  built it in December'94 -Jan'95.
It is shown here in test setup on a cold Sunday in January '95 after 
performing beautifully in its first and only powered test to date the 
evening before. This coil threw an 18 foot long streamer, recorded on 
videotape (see ltc04rws.jpg), with just 10 kVA of input power.  The 
mains service available during this test was only 40 amps@230 volts. 
The secondary is wound with 4200 feet of #12 THHN stranded copper wire,
close wound to a length of 67.5 inches on an open concept form. Operating 
frequency with large 67 inch x 15 inch aluminum torroid is 54KHz. Primary 
is 12 turns of 3/4 inch aluminum CATV distribution coax.  System resonated 
at 9 turns with two parallel Condenser Products Co., 0.025 uF,  60KVDC pulse 
discharge caps (polypropelene & silicon oil) shown under grounded strike 
shield..  Rotary break is behind the caps. The 10KVA, 16000 volt pole pig 
was left inside the lab and the HV was brought out to the coil on a length 
of RG-214 coax.

ltc02rws.jpg
Large 67 inch by 15 inch topload toroid with extended coil protection 
ring.  Shown upside down.

ltc03rws.jpg
Here I am trying to estimate the length of some streamers that hit 
the ground early during the test with a tape measure.  Coil stands 9 
feet tall to top of toroid discharge terminal.  

ltc04rws.jpg
An 18 foot streamer to air at just 10 kVA input power.  This is the 
longest streamer I have created with a Tesla coil to date.  This is 
more remarklable when you factor in the cold , dry dense air at minus 
20 Centigrade, January 1995.  Coil stands 9 feet tall to top of 
toroid discharge terminal.

ltc05rws.jpg
A very high energy 11 foot streamer strikes the ground. Coil stands 9 feet 
tall to top of toroid discharge terminal.

ltc06rws.jpg
Convoluted streamer upwards to air. Discharge toroid is 67 inches 
across.