Ti-Tan!! Specifications

Motors

4 x  Pittman  GM9236S020  24 volt motors

236 No Load RPM

PTC Thermal Resettable Fuse Protected

9.5 in-lbs running torque  (1.75Amps)

31 in-lbs full torque  (5.5 Amps)

54 in-lbs stall torque  (9.64 Amps)

Batteries

2 x  Panasonic LC-R122R2P  72 kJoules

12 volts

1.76 lbs

6.968 x 1.339 x 2.362 in.

1 Amp  4500 A-s

5 Amp  3000 A-s

10 Amp  2700 A-s

Ti-Wrex!! Standard charging/test port

30 Amp Auto Maxi hard fuse protected

Drive

Dual tank style tread drive

4 x 1 in wide x 3 in dia 24 tooth 3/8 pitch timing belt pulley

4 x Delrin drive cogs inner bore 5/8 dia brass insert

2 x 24 in cir 1 inch wide  3/8 pitch  64 tooth  Timing Belt

Tread  1 wide x 1/2 inch thick  Sorbothane (50 durometer)

Attached with Elmer's Pro-Bond Urethane glue

Frame

2 x 0.063  6Al-4V titanium support rails

2 x 0.032 6Al-4V titanium covers

WaterJet cut

Drive Force

0 lbs minimal at 49.5 in/s  (0.8 Amps)  (0.1 HPin)

19 lbs nominal at 37.7 in/s  (7 Amps)  (0.23 HPin)

62 lbs full at 28.3 in/s  (22 Amps)  (0.7 HPin)

108 lbs stall at 0/in/s  (38.5 Amps)  (1.2 HPin)

Turn speed (full) 1.5 RPM