Terry Fritz  2/2001

Description:

The Tesla Coil Tuner (TCT) is a simple and low cost signal source that can be used to find the resonant frequencies of the primary and secondary circuits of Tesla coils.  It uses simple commonly available parts.  It can be assembled in an hour or so with minimal electronic skills.  The cost of all the parts is about $20.

The TCT is simply a LMC555 IC square wave generator.  An audio taper pot and a 2% polypropylene timing capacitor control the 50% duty cycle oscillator's frequency.

A bi-color LED in series with the output senses the current being drawn and a frequency dial indicates the frequency setting.

Parts List:

QTY	Description					Part Number		Cost

2	Sets red / black alligator clips		RS 27-1545		2.99 / 3 sets

1	Large knob					RS 274-0433		1.29 / 2

1	Bi-Color LED					RS 276-012		1.19

2	10uF  16V  tantalum capacitors		RS 272-1436		2 x 0.79

1	LMC555  CMOS IC timer chip		RS 276-1718		1.39

1	8 pin IC socket				RS 276-1995		0.59 / 2

2	470 ohm  1/2 watt resistors		RS 271-1115		0.49 / 5

1	1.8nF  50V  Polypropylene 2% cap	DK P3182-ND	0.39

1	10K  Audio taper pot with switch		RS 271-215		1.99

1	Plastic box					RS 270-1803		3.29

1	Battery Clip					RS 270-324		1.89 / 5

1	Battery Holder				RS 270-326		0.99 / 2

1	Proto Board					RS 276-148		1.49 / 2

All parts can be purchased from Radio Shack (part numbers given here) or practically any other electronics parts supplier.  The timing cap is from Digi-Key and is rather critical.  The rest of the parts are non-critical but the pot should be of good quality.  Wiring, layout, and construction are not critical but try to keep the wire lengths reasonably short.

Schematic Diagram:

Assembly:

There are many ways to put the TCT together and it will work fine.  For those less familiar with assembling things like this, I will describe how I did it.

Box:  I selected the plastic cover and located two points on the cover.  The first was two inches from the bottom and the other one inch from the top.  I drilled a 1/4 inch hole at the bottom mark and enlarged it a bit to fit the 10k pot.  I then snapped the little tab off the pot with pliers and mounted the pot.  I connected a 470 ohm resistor to the center leg of the pot.  I drilled a 3/16 hole at the top mark and was able to force the bi-color led into it.  I added a bit of epoxy to hold it in place.  I also epoxied the battery holder in the bottom half of the box.  I cut a 2.25 x 2.25 inch square of poster board and cut a hole in it and glued it to the box to mark settings on.  I used water soluble wood glue incase I ever wanted to change it.  I then installed the knob.  In the bottom of the box, I drilled two 9/64 inch holes for two 8 inch lengths of wire to act as test leads.  I tied and epoxied the leads to the box and installed alligator clips to the ends.

I used two other alligator clips to make a 6 inch jumper to short the spark gap for primary testing.

Circuit:  Snap the two circuit boards in half and solder the 8 pin socket in the center of one.  Following the schematic, solder the components to the circuit boards noting that S1, R2, R3, LED1, and the battery are mounted off the board.  Use hookup wire to make the needed connections and bridge the pads with solder where needed.  I put leads on the parts that lead off the board.

Calibration:

The timing capacitor is accurate to within 2% and the IC is fairly accurate internally.  Since there are stray capacitances in the circuit, it needs to have the scale calibrated with a frequency counter or voltmeter with that function.  If you don't have a frequency counter, you can still use the TCT to compare primary and secondary tuning.  Evenly mark off reference marks on the dial.  Lower frequencies are clockwise and higher frequencies are counter clockwise.

Operation:

The TCT is very easy to use for primary and secondary frequency measurements.  Obviously, these test should be done will all power removed from the coil and all capacitors completely discharged!  The procedures follow:

Insure all power is removed from the coil and all the capacitors are completely discharged!

Testing the TCT:  To tests the TCT's operation, connect the two test leads together.  The LED should light and remain lit through the entire frequency range.  Replace the battery if the light is dim.

Secondary Fo:  To test the secondary's fundamental frequency, simply connect the TCT between the ground and the base wire from the secondary as shown below.  Slowly turn the frequency through the range until the brightest spot is found.  The lowest and brightest frequency spot is the fundamental.  You may see the dimmer 3rd harmonic at ~3 x Fo.  It is probably best to test the secondary frequency on the coil in the actual configuration since the secondary frequency is sensitive to the surrounding objects.

Primary Fo: To test the primary circuit's frequency, simply connect the TCT across the primary cap and short the spark gap with the jumper lead as shown below.  Slowly turn the frequency through the range until the dimmest spot is found and read the frequency on the dial.  You may want to ground the top terminal of the coil to prevent the secondary from affecting this test.

Notes:

The author / designer of this device specifically releases all aspects of this design to the public domain.  It may be copied, sold, plagiarized, constructed, mass-produced, etc. for the good of Tesla coiling.  As far as I know, it is safe, works, and not much can go wrong, but I disclaim all responsibility...

Any questions or suggestions can be directed to:  terry@hot-streamer.com

Terry Fritz

February 7, 2001