Jyske EMC K232289

R&S ESPC. RF Field Emission.

EUT:                 E.u.T.

Manufacturer:

Operating Condition:

Test Site:           10m Vertical

Operator:            Hans V. Erichsen

Test Specification:  EN 50081-2 Generic Emission.

Comment:             BG noise

Start of Test:       21-09-2001 / 12:23:30PM

SCAN TABLE: "SH B237 INfie. farst"

Short Description:            RF-Field Emi 1ms

Start      Stop       Step       Detector  Meas.    IF      Transducer

Frequency  Frequency  Width                Time     Bandw.

30.0 MHz   60.5 MHz   50.0 kHz   MaxPeak   1.0 ms   120 kHz CBL 6111 JKO 237

60.5 MHz   122.0 MHz  50.0 kHz   MaxPeak   1.0 ms   120 kHz CBL 6111 JKO 237

122.0 MHz  246.0 MHz  50.0 kHz   MaxPeak   1.0 ms   120 kHz CBL 6111 JKO 237

246.0 MHz  496.0 MHz  50.0 kHz   MaxPeak   1.0 ms   120 kHz CBL 6111 JKO 237

496.0 MHz  1.0 GHz    50.0 kHz   MaxPeak   1.0 ms   120 kHz CBL 6111 JKO 237

MEASUREMENT RESULT: "K232289_001_fin QP"

21-09-2001  12:33PM

Frequency    Level  Transd   Limit  Margin  Height  Azimuth  Polarisation

MHz   dBµV/m      dB  dBµV/m      dB      cm      deg

30.450000    35.30    18.4    40.0     4.7     0.0     0.00  ---

31.400000    35.20    17.9    40.0     4.8     0.0     0.00  ---

91.750000    39.80     9.5    40.0     0.2     0.0     0.00  ---

98.500000    43.20    10.3    40.0    -3.2     0.0     0.00  ---

100.650000    40.10    10.6    40.0    -0.1     0.0     0.00  ---

101.200000    47.40    10.6    40.0    -7.4     0.0     0.00  ---

101.750000    42.80    10.7    40.0    -2.8     0.0     0.00  ---

103.000000    37.10    10.8    40.0     2.9     0.0     0.00  ---

104.150000    44.70    10.9    40.0    -4.7     0.0     0.00  ---

105.650000    29.50    11.1    40.0    10.5     0.0     0.00  ---

106.650000    40.90    11.2    40.0    -0.9     0.0     0.00  ---

107.500000    67.60    11.3    40.0   -27.6     0.0     0.00  ---

169.700000    53.70    10.2    40.0   -13.7     0.0     0.00  ---

343.350000    51.90    16.1    47.0    -4.9     0.0     0.00  ---

464.350000    51.20    19.2    47.0    -4.2     0.0     0.00  ---

464.750000    53.50    19.2    47.0    -6.5     0.0     0.00  ---

467.950000    39.80    19.3    47.0     7.2     0.0     0.00  ---

511.250000    64.60    21.4    47.0   -17.6     0.0     0.00  ---

512.100000    38.00    21.5    47.0     9.0     0.0     0.00  ---

512.800000    44.80    21.5    47.0     2.2     0.0     0.00  ---

516.750000    50.60    21.5    47.0    -3.6     0.0     0.00  ---

517.300000    42.80    21.5    47.0     4.2     0.0     0.00  ---

623.250000    31.10    24.1    47.0    15.9     0.0     0.00  ---

751.250000    63.00    26.4    47.0   -16.0     0.0     0.00  ---

756.750000    41.80    26.3    47.0     5.2     0.0     0.00  ---

935.600000    61.30    28.9    47.0   -14.3     0.0     0.00  ---

936.550000    61.40    28.9    47.0   -14.4     0.0     0.00  ---

941.750000    65.50    29.2    47.0   -18.5     0.0     0.00  ---

948.550000    66.20    29.5    47.0   -19.2     0.0     0.00  ---

956.550000    66.40    29.5    47.0   -19.4     0.0     0.00  ---