BIPOLE2.GIF

This 800x600 scan shows a rough looking Tesla workstation set up
with a bi-polar coil. The rolling table has shelving space below
for fourteen homemade poly-AL-oil capacitors, though only four
capacitors occupy the shelf in this image. Later a small shelf
was added to the side of the table for the spark gaps. This table
is equipped with a massive grounding system and has a built in
counterpoise. Below the table top there is a heavy brass plate.
The brass plate has a short length of one inch ground strap
soldered to it. This ground strap may be passed through a slot in
the table top to make a direct connection with the base of the
Tesla resonator. The heavy brass plate is grounded via four
parallel lengths of #6 cable, one going down each leg of the
table, and connecting to 1/8-inch alumnium plate screwed down
below the capacitor shelf, about one inch from the floor. This
aluminum plate acts as a small counterpoise and gives the
illusion to the coil that true ground is directly beneath it.
The counterpoise is connected with several sections of ground
strap to an electrically isolated hydraulic car lift control just
outside the garage door. This ground is better than the one used
by Tesla in Colorado Springs.

On top of the table to the right sits a cylinder spark gap. Just
left of the gap there is a rubber inner tube and pieces of
plastic and wood for winding temporary primary coils used for
testing and experimentation prior to construction of permanent
coil forms. Solid polyethylene core coax (RG-213) comes in from
the bottom left of this image to bring high voltage from the
power supply up to the cylinder spark gap.

Plastic cord is hung from the rafters to support a five turn
helical primary coil wound from 3/8 inch copper tubing on a
wooden coil form lined with plastic insulation.

The secondary coil is a long skinny "candlestick" design from the
late 1960s or early 1970s. The coil is wound on a plexiglas tube
five inches in diameter using about 650 turns of PVC jacketed
solid core bell wire that wound at about 18 turns per inch. The
actual winding was 36 inches long giving this coil an aspect
ratio of 7.2, and an approx. resonate frequency of 530 kHz.
This coil was a disaster when fired in a 1/4 wave configuration.
The design is inefficent and the coil coupled very poorly to
every primary I tried with it. Having a high resonate frequency
it would not accept much power, and when overdriven the resonate
frequency of the coil would split, with several 1/4 wave voltage
peaks appearing in the winding and sparks jumping out from
everywhere but the discharge terminal.

The coil finally did find use as a half-wave coil. I wrapped the
coil up in a couple of rolls of plastic food wrap to help
insulate, then set it on it's side across two saw horses. The
resultant bi-polar coil proved much more efficient, and opened
the door to wide range of investigations with RF transmission
lines, extra coils, and bi-phase coil systems.

 System was designed and built by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA