PICA1024.GIF and PICA800.GIF 

 These are 1024 x 768 and 800 x 600 scanned photos of my 10 inch  
 coil firing at 2880 VA. The toriod is 20 x 5 inches, the longest 
 spark recorded here is 72 inches. The coil is powered by a       
 parallel bank of 12 kV neon sign transformers. Spark gap system  
 consists of a small rotary gap in series with two cylinder       
 static gaps. The primary coil was 8.8 turns of 1/2 inch copper   
 refrigerator tubing, and the tap was set all of the way out. The 
 tank circuit capacitance consisted of fourteen homemade rolled   
 capacitors. The value of each cap is ~.019 microfarad rated at   
 ~10 kV pulse; seven capacitors were placed in parallel for a     
 value of .133 microfarads, and one bank was placed in series on  
 each side of the primary. The measured capacitance was .0665     
 microfarads rated at about 20,000 AC volts pulse.

 The ten inch secondary coil is wound on sealed PVC pipe, with    
 just over 1000 turns of number 21 AWG double Formvar coated
 magnet wire. Winding length is 32 inches. The system as          
 pictured here resonates at about 125 kHz. 
  
 Photo is a one second exposure on Kodak ASA 400 film. Longer
 exposure times bring out the background detail, but superimpose
 the sparks to the point they lose definition.
  
 System was designed, built, and operated by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA