PICK1024.GIF and PICK800.GIF

 These two scans (1024x768 and 800x600) show a "bargin basement"
 coil producing about twelve inches of spark. The secondary coil
 is wound with enamel covered magnet wire on a four inch diameter
 thin wall PVC plastic drain pipe. The plastic pipe was sealed with
 several coats of polyurethane before the coil was wound, and the
 coil was coated again with several coats of sealer over the
 windings to reduce corona loss. The discharge terminal is an
 inverted stainless steel measuring cup that lacks a handle. The
 discharger is taped to the top of the secondary with several turns
 of black electrical friction tape.

 The primary coil is eight turns of three-wire electrical extension
 cord that has all three conductors fused at the ends. The eight
 turn primary is a "flat pancake" (Archimedes spiral) wound on a
 coil form constructed of plexiglas strips mounted in a simple
 hardwood frame. Pegs cut from wooden dowels are plugged into holes
 drilled in the plexiglas strips to act as spacers between primary
 turns.

 The spark gap is a cylinder static gap constructed from 14, two
 inch long sections of 1-inch diameter hard copper water pipe
 mounted inside of a short length of standard six-inch PVC drain
 pipe. Air flow through the pipe is provided by a small muffin fan.
 Only seven gaps are used, with the spacing between electrodes set
 at about .030 inches.

 The capacitors used in this coil project are homemade salt-water
 capacitors constructed using stacks of five gallon polyethylene
 plastic pickle buckets filled with brine. The designer/builder
 stated to me that he was very pleased with the capacitor
 performance vs. time and money, and indicated he has operated
 these capacitors at power levels up to 8 kVA using a reversed
 power distribution transformer running 15 kv into the tank circuit
 for extended periods without failure. He noted the salt water has
 a very high heat capacity which prevents hot spots from forming.
 He also stated the salt water appeared to boil at higher power
 levels due to the electrical pulsing (not heat) and that a heavy
 layer of cheap motor oil over the exposed brine reduced the corona
 losses.

 The power supply for the scanned photo here was a pair of 12 kv
 neon sign transformers in parallel. No voltage control was used.

 This coil was designed, built, and operated by: Dave Hartwick
 191 Highland Rd., Chambersburg, PA  17201  USA