Here is a shot of the inside of one of the pigs with the lid
opened and rotated to the side. Due to the problems with
focusing, lighting, and refraction in the oil I have labled
various major structures for clarity.

A, B, C, = These are the low voltage ceramic bushings right at
           the oil level. The center bushing is usually grounded/
           neutral with 240 volts obtained all the way across
           A - C.

D = This is the single HV ceramic bushing extending downward
    through the lid of the can into the oil. A HV lead wire
    wrapped in kraft paper insulation comes up from the winding
    and the connection is made under about 8 inches of oil.

E = The is the core frame. Not shown is the second end of the HV
    winding which is usually bolted directly to the top of the
    frame. This other end is accessible and can be freed to
    convert a pig where two HV terminals are required.

F = Linkage assembly for the oil submerged breaker. A ring lever
    is mounted on the outside of the can where a lineman equipped
    with a long pole and end mounted hook can pull down and reset
    the unit.

G = This is the oil submerged breaker assembly bolted to the top
    of the core frame.

H = These are the high current copper or aluminum busses that
    connect the LV terminals/breaker assembly/windings. These
    busses are insulated with heavy wraps of high quality kraft
    paper.

I = This is a poorly focused lightning arrestor inside of the
    can. It is bolted directly to the inside terminal ends of
    bushings A, B, & C. This could easily be removed as it serves
    no real purpose in Tesla applications. In line service
    bushing "B" would be earthed, and arrestor "I" provides a
    path for HV to ground that would give some safety margin.


Richard Quick